## Slide 1: Context & Group Addressing
Jason Tam Scott Xu David Shen
http://summer.winlab.rutgers.edu/projects/wiki/2012/Projects/MobilityFirst/Context

## Slide 2: Purpose
Explore applications of group addressing and context aware messaging in the MobilityFirst framework
New branch of applications opened up
Group by sensor data context

## Slide 3: Architecture

## Slide 4: Data Server - PHP Query Construction
1_KR3DM 3-axis Accelerometer.csv
  Delimited by an underscore to determine table to insert into
`timestamp`,`x`,`y`,`z`
  Comma delimited field names for insertion field
1345066313885,-0.77469909,-0.3807226,9.442732
  Insertion values
[id, GUID, and ip added]
Final query to run
  INSERT INTO `1`(`timestamp`, `x`, `y`, `z`, `id`, `guid`, `ip`) VALUES (1345066313885, -0.77469909, -0.3807226, 9.442732, A000002241E787, 30B57BFBB820273207483858911A00377BD558A3, 174.226.197.69)

## Slide 5: Data Server - MYSQL Contents

## Slide 6: Robust Upload
Division of file into chunks
Grab last successfully uploaded timestamp
Timeout & increase wait time

## Slide 7: Data Server - Scalability
Replication (simple)
  Default LAMP install
  Include our php scripts
  Initialize

## Slide 8: Archival Resolution
Queries data server to determine membership
App determined (may or may not result in an addition/removal from GCRS)

## Slide 9: Immediate Resolution
Uses immediate data pull to determine membership
Client reads app’s def file
Client adds/removes itself

## Slide 10: Abstraction for Apps
Combine base contexts
  Create new (app specific) context
  GCRS assigns group GUID
Apps needs only to communicate with group GUID for messaging
U4BZ7EFBXF6W173817483778HE1R05327BD55923

## Slide 11: Prevailing App Idea
‘iClicker’
  Address truthful attendance issue
  Novel context reliant features

## Slide 12: Smartphone (Indoor) Localization
[mini digression]

## Slide 13: Smartphone (Indoor) Localization
GPS
  Unreliable indoors
Wifi trilateration/SVM
  Requires multiple WLAN
Bluetooth
  Self sufficient for dense networks
  For all phones
    Set discoverable
    Discover
    Send results (MAC & RSSI) to server to compute

## Slide 14: Algorithm Test with Generated Grid
Grid truths
Localization Algorithm
[Modified Algorithm via Robust Distributed Network Localization with Noisy Range Measurements, David Moore, John Leonard, Daniela Rus, Seth Teller MIT Computer Science and Artificial Intelligence Laboratory; 2004]

## Slide 15
Chart: Bluetooth RSSI vs Distance
| 0 | 5 | 10 | 50 | 100 | 200 | 300 | 525 | 975
NS4g Reading DX | -25.3333 | -19.3 | -32.4 | -46.4848 | -49.3208 | -61.6 | -64.5263 | -71.4324 | -74.7826
DX Reading NS4g | -41.9444 | -35.9167 | -50.704 | -59.5825 | -65.8049 | -80.4946 | -81.8571 | -92.5946 | -95.5321
Formula@+20dBm Pt | 19.948 | -0.052008 | -20.052 | -34.0314 | -40.052 | -48.0108 | -54.0314 | -60.052 | -63.5738 | -66.0726 | -68.0108 | -69.5944 | -70.9334 | -72.0932 | -73.1163 | -74.0314 | -74.8593 | -75.615 | -76.3103 | -76.954 | -77.5532 | -78.1138 | -78.6404 | -79.1369 | -79.6065 | -80.052

## Slide 16: RSSI -> Distance
[Formula via Indoor Location Using Trilateration Characteristics, B Cook, G Buckberry, I Scowcroft, J Mitchell, T Allen, 2005 ]

## Slide 17: Anchor Points
One globally positioned -> all globally positioned
Wifi localization can resolve ambiguities

## Slide 18
?